Material Selection

LINTEL

Beam: $250 plus shipping
S8x18.4#, 10 feet long
(184 lbs)
Outside width: 4.001 inches
Taper angle:

ADJUSTABLE BEAM SUPPORT

INSIDE POSTY BIT:
3 ½ by 1 ½ leaves 1/8 clearance total (1/16 per side)
1/8” wall thickness

CAPS 3/8 plate

CROW’S FOOT SECTION
OUTSIDE SLEEVEY BIT:
4x2x.188
inside clearance: 1 5/8 by 3 5/8
Support along 1/3 of	height

Welds:
min fillet on 1/4” member is 3/16 per AWS D1.1
Min fillet on <1/4” member is 1/8 (but make it 3/16)

HARDWARE:
- Tapered washers for bolting through bottom of beam
- Grade 8 hardware stack:
Bolts -
Tapered washer, nom ¼ thick @ center - 91152A035
I -beam nom. Thickness – 0.426 (tapered on this)
94895A835 – nuts – 3/64 height

- Casters: 2408T158 mcmaster
- Pad eyes:
53CV52 granger model – min 1” hole needed

HOIST:
Low-headroom chain hoist:
http://www.globalindustrial.com/p/material-handling/hoists-cranes/hoists-manual-chain-lever/low-headroom-hoist-trolley-combo-manual-2000-lb-cap?infoParam.campaignId=T9F&gclid=EAIaIQobChMI_fLboOGZ2QIVAUOGCh22uwHoEAYYAyABEgK5NvD_BwE
$342 – can be a later addon

Lever hoist: https://www.amazon.com/VEVOR-3000LBS-Ratchet-Manual-Puller/dp/B01MTGIKB8/ref=pd_cp_328_1?_encoding=UTF8&pd_rd_i=B01MTGIKB8&pd_rd_r=DXP9N4NC1KNVKCCYN116&pd_rd_w=nXKwH&pd_rd_wg=AUjpd&psc=1&refRID=DXP9N4NC1KNVKCCYN116
$129

Independent 2-ton Trolley : $135 https://www.ebay.com/itm/2-Ton-Push-Beam-Trolley-Adjustable-for-I-beam-flange-width-4-to-8/122822247556?epid=1000622037&hash=item1c98c6c484

Vestil LOW-4G Geared Low Headroom Combination Chain Hoist/Trolley, 4000 lbs Capacity, 3-1/2"- 8" I-Beam Flange: 691215077439