2 ton gantry lift

Prior Art / model type:
http://www.lkgoodwin.com/more_info/a_series_gantry_crane/a_series_gantry_crane.shtml

10ft span (outside)
Minimum Clear span 8’10”

Minimum 7’ high
Maximum 11’ high

Caster spread – 6’ 6”
Wheel diameter – 8”

IMPORTANT SAFETY INFORMATION
Method of lifting
- This crane will be designed for vertical, unguided loads only.

- As flipping a mill over on its back is one of the goals for the gantry, this will have to take place with two hoists – one at the top, the other with a sling at the bottom. As one ascends, the other can descend to safely manipulate the casting.

- The 10ft clearance of the gantry should facilitate this kind of thing.

Moving Load
Should this move on the casters?
What kind of casters should it have?

STANDARDS
Test Standard
ASME B30.2 – Test to 1.25x capacity (5000lb)

Design factor of safety -

AWS has allowable unit stresses in weldments?
AISC publishes unit stresses for steel structures

Per Marks, p. 419 in section 5, “strength of materials”

ASME B30.16 – hoists (hoist should follow this)
ASME B30.17 – Cranes and Monorails (design to this)
ASME B30.2 - gantry cranes (design to this)
https://www.asme.org/products/codes-standards/b302-2016-overhead-gantry-cranes-top-running