WELDING CONNECTION:

LEG:
23" section of 4" square tube, 4" out of top for pin hole
5'5" of leg

19" between top of leg and bottom of leg

1/8" fillet on 1/8" material
7018 has tensile strength of 70,000 psi
A36 has a min yield strength of 36 ksi and 58-80ksi ultimate tensile strength

THE RESEARCH QUESTIONS:
- What are the definitions of t, y, k, and cross connections?
- What kind of connection are we looking at?
- We are dealing with a truss-like connection, which would be a shear connection.
- What is the allowable strength of a lap weld in tension?

- What is the buckling strength of a T-connection at 35 deg in tension?
Relevant section: p. 16.1-140; chapter K, section 3b "specification for structural steel buildings"

- What is the allowable tension on a joint of mismatched 1.5" and 2" 1/8 wall tubing?
- What is the punch strength of the tubing?

THE HARD QUESTION:
- What is the allowable strength of a lap weld in compression?
- How would I analyze the compressive behavior of the split 4" column?